## Slide 1: CPR Aylth Roundhouse and Diesel Depot
John Duncan

## Slide 2: CPS “Empress of France” – Gladstone Dock June 1956

## Slide 4: Train No 7 ‘The Dominion Montreal to Vancouver
F A& B unit plus GP9 with 4625 steam Generator
Potage de Prairie

## Slide 5: First view of Alyth Roundhouse
From the wood bridge to the stockyard
Locomotive 5910 Selkirk, T1a 2-10-4

## Slide 6: First close up of a G3g Pacific
Big in height and width
In for yearly exam

## Slide 7: East end of Alyth diesel shop fuelling points

## Slide 8: 1929 built T1a 5914 at oil fuel road Alyth
Private brass foundry behind

## Slide 9: 5927 the last T1b before scrapping
Filling up with 4100 gallons of Bunker C Oil

## Slide 10: Dimensions of Selkirk T1b 1938 build

## Slide 11: P2k 5469 2-8-2 1948 build at Alyth

## Slide 12: H1c 2833 4-6-4 Royal Hudson
Just off Edmonton mail, night shift , initial exam

## Slide 13: G3g 2448 4-6-2 at Alyth incoming road
Worked Calgary to Lethbridge road

## Slide 14: Overhaul of No4 Nathan LH lubricator
Setting Nathan DA valve 25 psi above max boiler pressure at 300 psi

## Slide 15: 5465 P2K 2-8-2
Top of superheater element and throttle valves, whistle. Smoke stack and coil type feedwater heater

## Slide 16: 5465 P2K,2-8-2
Smoke box front and cowl after 12 monthly examination and test of elements and examination of throttle valves (nuts on top of element bolts)

## Slide 17: Safety valves on 5933 set at 285 psi

## Slide 18: Yearly exam and inspection, moving parts on motion
Whitewashed for cracks – scotching chains

## Slide 19: T1c 5931 on heavy freight on Brooks Division
East of Calgary up to 1500 tons

## Slide 20: A floating bearing 9 ½” inside dia 12”outside dia
On T1 big end bearings.
Fitted at Medicine Hat

## Slide 21: September 1956 on nights 12 – 8 am.
Switcher Machinist
My helper Michael Wislovich (Polish-Canadian).
I was called a limey

## Slide 22: 5800 at 27degree F
With Eddie Keener, fireman and Walter Dempsey switchman

## Slide 23: 6269 V5a hump engine
Engineer Carl Wilson (Mr Leak only at 8 am)

## Slide 24: 597 Dpc 4-6-0 the oldest switcher
Alco 1903

## Slide 25: 3616 N2a 2-8-0 switcher ex Ogden shops.
The cylinder blow crack seat in upper throttle valve removed and sent to shops

## Slide 26: 922 D10g 4-6-0 became a switcher
Converted to Walchaerts valve gear

## Slide 27: 3404 M4a 2-8-0
Best switcher, went east to Windsor Ontario in 1958

## Slide 28: 1282 G5d CLC 1948
Coal fired on Kneehill mixed.
9 years old at Alyth taking on water during firemens strike

## Slide 29: First inspection job after passing air brake exam
On 2864 for the Edmonton mail.
On the afternoon shift from 1600 to midnight

## Slide 30: Brake examination in October 1958 for steam & diesel locos certification

## Slide 31: 2863 RH side of the cab, showing foam meter
Indicating foam forming at the top of the boiler water level

## Slide 32: 2863 showing foam blow off and dynamo

## Slide 33: 2863 Crosby bell and ringer

## Slide 34: 2863 Fireman’s gauges
Boiler pressure
Steam heat
Water pump pressure
Booster engine pressure

## Slide 35: 5933 for scrap 2863 East for traffic and special job in 1959
Queen Elizabeth and Duke of Edinburgh visit?

## Slide 36: GM Gp9 with OK 4625 steam generator & 2nd Gp9
8509 & 8533

## Slide 37: Boilermaker fitting Vapor Clarkson OK4760 steam generator coils in an F unit

## Slide 38: Kicking Horse Pass spirals

## Slide 39: Call out on G9p dynamic brake fault 2nd unit Gp9.
Stopped at Yoho loop between the the Mount Stephen spiral and Cathedral Mountain spiralto let train No8 through

## Slide 40: Gp9 dynamic brake grid out
Left to right
John - machinist
Joe – electrician
Bill – electrician
Fritz - machinist

## Slide 41: 5931 – 1959 going to Heritage Park, Calgary

## Slide 42: Dad and son Bill 2 ½ with 5931 in 1959

## Slide 43: SS Empress of France homeward bound for Liverpool Pier Head, December 1959

## Slide 44: Aylth Diesel Shop