## Slide 1: The Ultimate Steam Locomotive
David Pawson

## Slide 2: The Ultimate Steam Locomotive- a 20 year Personal Odyssey.
20 years ago the Ultimate Steam website said: ‘This fact, (lack of fully optimised performance) more than any other factor, is what led to the downfall of world steam.’
This says there is plenty of upward efficiency space beyond steam age best practice, and a much faster and more powerful ‘Ultimate Steam Locomotive’ is possible. How exciting!
Have spent 20 years procuring and developing first principles models, validating against Rugby, Swindon Altoona and Vitry data to see if true.
A recent spur was K3/K6 project claim they could build a 130mph 2-6-0.
So what is the limit of the possible, could the best make steam viable, and where should the ASTT focus its efforts?
The Ultimate Steam Site now lists 47 developments taking place around the world in the last 40 years.
  42 refer to improved exhaust, mostly Lempor.
  9 mentions of GPCS, none since 1991.

## Slide 3: Presentation Objectives
To identify, for steam locomotives:
  Factors that influence their drawbar efficiencies and power .
  Available technologies that could make a big difference.
  The scope to improve existing types and create better designs.
  The limit of the possible with fire tube boilers- the Ultimate.
Focus is main line types, but principles apply to smaller scales.
  Note: Improved Efficiency and power was a consistent design for 125 years!- no lack of creative genius or effort, just no reliable quantitative theory.
  Better Efficiency made a big difference in the 1930s. At 4000lb/hr hard coal:
    A low superheat Castle (1923) delivers ca. 1490/1020 IHP/EDHP at 70 mph.
    A streamlined, high superheat, wide grate Kylchap A4 (1938) ca. 2190/1720.
  In the 1950s, BR didn’t want more power, but better efficiency to do the same work more cheaply.

## Slide 4: Measures of the Thermal Efficiency
Usual measure is Drawbar Efficiency -the % of heat in fired coal appearing at the drawbar as useful work.
Two measures – raw DHP basis (DBE), based on road tests (e.g. 1948), simple to obtain, but can’t be reduced to an efficiency vs cut off and speed map- results depend on line, load and schedule. Good for A vs B, unless B goes faster!
Efficiency maps, as in BR Bulletins, must be based on EDHP, (EDBE), as used here. With these, efficiency on any load, line and schedule can be calculated.
  EDBE is numerically better than DBE if you want to compare apples and pears!

## Slide 5: Equivalent Drawbar Efficiency is low, and overstates the true value.
EDBE of best designs was low, peaking around 9% in the ‘sweet spot’ of moderate boiler outputs, speed ca. 50mph.
At higher express speeds, efficiencies were at best 7.5%.
EDBE does not include coasting, standby, preparation and disposal losses. (DBE includes first two), so true overall coal based thermal efficiency is overestimated.
Cox said by ‘10-15%’. WSR data suggest a factor of two on their line! Factors such as Loco size relative to work done and length of run influence this.
The Big Boy had DBE as low as 3% at full power!
Surely we can do better!

## Slide 6: Factors influencing EDBE
EDBE under constant operating conditions is the product of three factors:
  Boiler efficiency (BE)- the % of heat in the coal fired that finishes up as hot steam.
  Engine efficiency (EE)- the % of heat in the steam that is converted to useful work in the cylinders.
  Transmission efficiency (TRE)- the % of work done in the cylinders that appears at the drawbar on the level.
  EDBE= BE*EE*TRE

## Slide 7: Boiler Efficiency (BE)
Boiler efficiency (related to coal fired) is itself the product of three factors
  Grate efficiency (GE)- the % of heat in the coal fired that is released during combustion.
  Heat transmission efficiency (HTE)- the % of heat produced that finishes up as hot steam.
  Recycle efficiency (RE)- the % exhaust steam of water feed that can be recycled through the boiler.
  BE=GE*HTE*RE

## Slide 8: Grate Efficiency limits economic boiler output more than FEL
GE is related to loss of coal unburned or partial combustion to CO.
It is close to 100% up to ca. 400lbs evaporation/sqft/hr on hand fired boilers.
At higher rates it falls quite steeply, mainly due to the loss of unburned coal.
Unburned losses rise to ca. 20% coal fired at 750 lbs/sqft/hr- an economic limit usually not exceeded on a regular basis. Maybe also stress, cinder cutting? (Tests, e.g. Rooke, NYC Niagara , French Compounds, show more is possible!)
At very high rates there are additional losses as excess air falls, due to partial combustion to CO, but the boiler front end limit (FEL) pretty soon kicks in.
FEL depends on front end entrainment ratio- about 1000lbs/sqft/hr at 1.65
So boilers were sized to deliver maximum evaporation rates of no more than ca. 750lbs water/sqft/hr, with an entrainment ratio good for adverse conditions.
This applies for the good quality coals used in this country.

## Slide 9: Grate efficiency also depends on type of stoking, depth of firebed and coal quality
Mechanical stoking increases unburned losses, probably due to production of fines in screw feed. (Swindon showed fines in hand fired coal decrease efficiency). Losses similar in US and UK. These reduce boiler efficiency by about 10%.
Unburned losses can be reduced by working with a thick fire and increasing flow of secondary air, possible with Welsh coal. This may be linked to lower fire temperature.
This pushes the economic limit out towards 850lbs/sqft/hr.
GPCS could also help at high specific combustion rates, allowing more steam from smaller grates. (Data?)
With poor quality coal (e.g. used on Big Boys) unburned losses can be horrendous, hence dreadful BE/DBE.

## Slide 10: Heat Transmission Efficiency is good.
Three factors impact HTE:
  The loss of heat in the flue gases leaving tubes and flues.
  This has two components:
    the sensible heat of the waste flue gases, estimated from flue gas temperature- ca. 12-13%
    the latent heat of steam produced by combustion of volatiles (H) in coal, estimated from coal composition, ca.5%. Higher for oil, gas, wood, spent chip fat.
  Sundry losses e.g. Radiation ca.1-2%. (Canadian formula)

## Slide 11: Heat Transmission efficiency can be improved a little further.
Thus, HTE was generally around 80%, falling slightly as rate of working increased.
Can be improved:
  By lengthening tube plate distance, to lower exit gas temperature- a small effect. And, tube plate distances over 15’ reduce gases below 700o F at 600lbs/sqft evaporation and this lowers A and E type superheat- a larger efficiency loss. Counter flow e.g. Houlet better.
  By a device such as a Crosti preheater, which saves around half the sensible heat loss.
No real need for high surface area for good heat transfer!
No known practical way to capture latent heat losses.

## Slide 12: Recycling exhaust steam boosts boiler efficiency.
By recycling exhaust steam e.g. with an exhaust steam injector (ESI) or feed water heater (FWH), more steam can be produced for a given amount of coal fired, because the heat input to bring exhaust steam back up to working temperature and pressure is quite small.
The maximum amount of heat which can be recycled this way is of the order of 15%.
In practice, an ESI recycles about 6% steam, a FWH (which needs some steam to feed pumps) nets out at about 10%. Coal savings are a bit higher.

## Slide 13: Boiler Efficiency Summary
With waste steam heat recycle, a conventional boiler can achieve efficiencies of over 80% at normal operating rates.
Fire tube boilers are thus pretty efficient. They are not a major weakness. Well done George.
A Crosti boiler can raise this by about 5% by capturing otherwise lost sensible heat.
With best coals, the economic limit of hand fired boilers is around 750-850 lbs steam/ sqft/hr, one clear determinant of the maximum power a locomotive can develop.
Maximum steam at a given grate size is given by the best coal. Alternative fuels will deliver less.

## Slide 14: Engine efficiency- maximum possible determined by Second Law
The maximum efficiency of any steam powered device at a given inlet pressure and temperature and outlet pressure is fixed by the second law of thermodynamics. Entropy cannot decrease between inlet and exhaust!
For devices operating at the maximum temperatures and pressures possible from fire tube boilers (300psi, 430 deg C) expanding down to near atmospheric pressure, the maximum possible efficiency is around 20% only.
At more common maximum inlet pressures and temperatures of 250psi and 400 deg C, maximum possible efficiency is just over 18%.
Expanding steam of moderate temperature and pressure down to atmospheric is a bad idea! But in the 18th century, there was no choice-it changed the world.
With a water tube boiler working at 1200 psi, (e.g. CP 8000) this rises to 26%.
Expanding steam down to vacuum (as in power stations) is a much better idea, which is why much of Europe’s rail system remains steam powered.

## Slide 15: Maximum engine efficiency dependency on superheat and inlet/exhaust pressures
 | Inlet temp, deg F | Inlet pressure, psig | Exhaust pressure, psig | Overall thermal efficiency % | Lbs steam/ihp-hr
A | 550 | 240 | 3 | 17.0% | 11.6
B | 600 | 240 | 3 | 17.3% | 11.1
C | 650 | 240 | 3 | 17.7% | 10.7
D | 700 | 240 | 3 | 18.2% | 10.2
E | 750 | 240 | 3 | 18.6% | 9.8
F | 800 | 240 | 3 | 19.1% | 9.4
G | 800 | 290 | 3 | 20.0% | 9.0
H | 650 | 240 | 10 | 16.0% | 11.9
I | 650 | 170 | 3 | 16.1% | 11.7
J | 800 | 1200 | 3 | 26.3% | 7.0
K | 650 | 240 | -14.6 | 38.5% | 4.9

## Slide 16: Potential Engine efficiency in simple reciprocating engines is about 85% of the possible.
These efficiencies assume the device used achieves a perfect result- unchanged entropy, 100% Isentropic Efficiency (IE). Any real device will be worse.
Calculations show Britannia valves and cylinders fed at 25000lbs/hr, with no leakage or heat transfer losses, can achieve about 85% IE at low back pressure.
In reciprocating engines, the cause is irreversible expansion losses when steam flows through a valve to an area of lower pressure- filling the clearance space, wiredrawing during admission, and incompletely expanded steam to exhaust.
CV losses are small at speed; at low speed/ long cut offs, losses to exhaust are the problem; at speed the problem is wire drawing. Best results at short cut offs.
The effect of lap and lead is small. Poppet valves do not bring efficiency benefits in UK context, though may be lower maintenance.
Reciprocating engines are pretty good up to the pressures of firetube boilers!
One potential way to improve on the 85% is to adopt Compounding, but most French Compounds were in practice no better than simples.
Compound operation was essential in experimental designs with very high pressure water tube boilers.

## Slide 17: In real engines, we get less than 85%
Best Measured engine efficiencies are about 80% IE.
The difference of 5% between actual and potential IE is down to two factors, heat transfer losses and leakage.

## Slide 18: Heat transfer loss through cylinder wall condensation occurs at low superheat
For cylinders operating at thermal equilibrium (e.g. on a test plant), the only significant heat transfer losses are caused by condensation of steam onto the cylinder and valve walls at inlet. This re-evaporates without doing useful work as the steam in the cylinder cools.
This process occurs when the cylinder walls are below the saturation temperature of the inlet steam.
Data from Altoona show that cylinder walls become hot enough to eliminate all condensation at around 630o F inlet steam. Wall temperatures are highest in long cut offs.
So most latter day UK types do not suffer from under their designed high steam rate operating condition.

## Slide 19: Condensation losses do occur on low superheat types and at low steam rates
Rugby tests show that on UK size cylinders, condensation losses are ca. 1000lbs/hr/cylinder on saturated types, half that at GW 2 row levels around 525o F, small at GW 3 row levels of ca 580o F.
Thus, on simples, the condensation problem was largely solved by sufficient superheat, though at low rates of working, e.g. freight, preserved lines, when superheat is low, most types likely still suffer.
Condensation on the large LP cylinders of Compounds can be high even at HP inlet steam of 650oF- a minimum of 750oF is needed. This negates much of the benefit of Compounding.
Other heat transfer processes are too slow to affect efficiency over a single cycle. They may help to heat up cylinders. (Quasi) thermal equilibrium needs about 15 minutes it seems for superheated types.
So, as cylinders are warming up efficiency will be less (KLR tests!).

## Slide 20: Leakage losses
For latter day simples then, the best case loss of 5% isentropic efficiency from the ideal must be attributed to leakage.
Leakage, according to Wardale is the ‘great unknown’
Analysis of Rugby data suggests that on top condition BR Standards, leakage varies between 1500 and 3000lbs/hr- even between different members of the same class.
Leakage likely increases with the number of cylinders and valves. The four cylinder Duchess was leaking at up to 4500lbs/hr!
The analysis suggests that losses do not vary much with the rate of working, hence losses are proportionately greater at lower steam rates- easily 10-15% at UK rates of 15-20000lbs/hr.
It also suggests that leakage is multifactorial- losses both within and from the steam circuit, thus no magic bullet.

## Slide 21: Effect of superheat and BPP on engine efficiency, Britannia, 28/70, 28500lb/hr
Chart: Inlet steam, deg F
| 410 | 430 | 450 | 470 | 490 | 510 | 530 | 550 | 570 | 590 | 610 | 630 | 650 | 670 | 690 | 710 | 730 | 750 | 770 | 790 | 810 | 830
5.375" blastpipe | 1.4501 | 1.4036 | 1.3759 | 1.3305 | 1.2997 | 1.251 | 1.201 | 1.1661 | 1.1256 | 1.0907 | 1.0564 | 1.0202 | 1 | 0.9763 | 0.95252 | 0.93626 | 0.91999 | 0.90568 | 0.89115 | 0.87848 | 0.86675 | 0.85588
6.28" Lempor | 1.3746 | 1.3342 | 1.297 | 1.2615 | 1.2321 | 1.184 | 1.1449 | 1.1082 | 1.0707 | 1.0412 | 1.0102 | 0.98024 | 0.95845 | 0.93718 | 0.91535 | 0.90013 | 0.88404 | 0.87067 | 0.85775 | 0.84561 | 0.8343 | 0.8228

## Slide 22: Engine Efficiency Summary
A simple engine operating at UK best practice inlet temperature and pressure, with a low back pressure exhaust can in principle achieve engine efficiency of around 18.5*0.85= 16% under normal operating conditions.
Due to sundry leakages, this will in practice be nearer 14.5%.
Pushing the envelope of best practice (boiler pressure, superheat, backpressure)raises this figure to over 15.5%.
A 300 psi high superheat Compound could achieve 16.5%
A 1200 psi water tube boiler Compound could achieve 20+%.
The K3/K6 project assumes >100% isentropic efficiency!

## Slide 23: Transmission efficiency
  At constant speed on the level, Transmission efficiency (TRE)=(IHP-LR)/IHP%, where LR is the locomotive’s resistance in HP, measured at constant speed on level track.
  LR increases rapidly with speed, so TRE falls quickly.
  At a given speed, LR is more or less independent of power, so the higher the power developed (e.g. thanks to greater EE) the better the TRE.

## Slide 24: Factors influencing LR
LR is the sum of three components- aerodynamic resistance(AR), vehicle resistance(VR), and machinery resistance (MR) between the cylinders and wheel rims.
AR increases with the cube of speed. It is low at 20mph, but becomes dominant above 70mph.
It is determined by frontal cross section area and drag coefficient.
The front cross section of most locomotives tends to fill out to the loading gauge, so even small locomotives suffer from high AR- not weight dependent.
Streamlining can reduce drag coefficient, hence AR by 20%. Its benefit becomes important at speeds of 70 mph+.

## Slide 25: Vehicle and Machinery Resistance
VR is proportional to the weight of the locomotive. It is the smallest component, about 40% of the total at 20mph but only 20% at 70mph. The benefits of light weighting (e.g. 10%) are therefore small for express designs.
MR is a complex function of many factors.
  At low speeds, Journal friction and coupling rod effects dominate.
  At high speeds, Windage and rotating dynamic masses add their weight. Boxpox may help with Windage.
  There is a small dependence on the amount of power being developed in simples.
  On 4 cylinder compounds it appears that MR is much higher than simples, again limiting any benefit from Compounding.

## Slide 26: Benefit of light weighting -Gradient and acceleration effects on LR
The heavier the locomotive, the more work needs to be done to accelerate it to cruising speed and lift it up gradients.
This work is often destroyed by braking, which means lighter locomotives are in principle better. However:
  Acceleration work is a very small proportion of the total particularly on long runs. It is more important on stoppers.
  On lines with gradients of 1 in 125 or less (most UK main lines) all the work done against gravity going uphill can be won back down the other side without speeding. Gravity gives back what it takes.
So, the effect of locomotive weight is normally relatively small on EDBE, but it will limit uphill speed and acceleration.
A 125 ton 60163 (cf. Class 47) + 500 tons would be 16 seconds faster to Finsbury Park, 1 minute to Peterborough.

## Slide 27: Drawbar Efficiency Summary
Boiler efficiency is pretty good. Some upwards improvement beyond UK best practice is possible with feed heating, and a Crosti type preheater.
Transmission efficiency deteriorates quickly above 50 mph. Streamlining brings significant benefits at 70+mph. Light weighting not much of a deal.
Engine efficiency is a shocker. It’s not an engine design problem- simples deliver 80+% of the possible- the unflinching second law is the bugbear.
Overall, designs evolved to towards limiting values for BE, EE and TRE and best designs achieved EDBEs of 80+% of what is possible with a simple.
                In the absence of good theory, Steam age designers experimented boldly and came out in a great place, trading off capital costs, complexity, reliability and efficiency, and commercial needs. They didn’t miss any big tricks.
                There is no Pot of Gold at the end of the Rainbow. Nothing can change the underlying inefficiency of low pressure steam.

## Slide 28: Drawbar efficiency of a Peppercorn A1- current best practice +Ultimate options
Cut off % | Speed mph | steam rate, lbs/hr | IHP | engine efficiency | transmission efficiency | boiler efficiency | drawbar efficiency | Index
48.8 | 20 | 26025 | 1512 | 10.90% | 93.85% | 80% | 8.18% | 114
30.2 | 40 | 26031 | 1832 | 13.21% | 89.08% | 80% | 9.40% | 131
24.6 | 60 | 26026 | 1939 | 13.98% | 79.63% | 80% | 8.90% | 124
22.2 | 80 | 25970 | 1957 | 14.14% | 63.57% | 80% | 7.19% | 100
22.2* | 80 | 25970 | 1957 | 14.14% | 68.27% | 80% | 7.72% | 107
18.9** | 80 | 25976 | 2160 | 15.26% | 71.25% | 85% | 9.28% | 129
45/43*** | 80 | 26000 | 2265 | 15.68% | 72.41% | 85% | 9.81% | 136
* Streamlined ** add 300 psi, Houlet, feedwater heater, Lempor *** Ditto, 3 cylinder compound, 410 deg C inlet |  |  |  |  |  |  |  | 

## Slide 29: Ultimate Design Considerations
A series of incremental improvements with proven technology can bring up to 30% more power, but may involve higher costs or risks than steam age designers were prepared to take.
Compounding could add 7-8% to this, but there are uncertainties.
Is a 3 cylinder high pressure and superheat fire tube Hush Hush the Ultimate?
Lempor has slight efficiency advantages over Kylchap, no game changer.
The maximum power with hand firing means the practical cruise limit is 90mph- faster requires mechanical stoking or oil/gas.
NB. Designs built to a concept, not rooted in operational reality were unsuccessful (E.g. LNER P2, PRR T1, Q2)

## Slide 30: An Ultimate UK Express Steam Concept
An upgraded A1 design, 60164, powerful and robust enough to deliver consistent 90mph running, with long operating range, utterly reliable, low maintenance, friendly footplate. The ‘Go To’ machine.
Higher efficiency achieved as outlined above, (Thanks Mr. Woodard, Lima, 1925, M Chapelon, Sir NG, 1930s) but:
  No Crosti (Aesthetics!)
  Hush Hush Compound a bridge too far? (Sorry, M. Chapelon, Sir NG.)
Built like a tank
  High mechanical robustness, low servicing. (N&W 1950)- higher weight might require 4-6-4. (W1/2 60701?). NB tender to firebox distance too far on W1!
Uses components from existing designs, upgraded when necessary.
Traction control. High TE, out of the traps like a rocket.
Oil/gas/hydrogen fuelled to simplify servicing? No coal, so less efficient?
Large tender to accommodate extra supplies for 200 miles, and hotel power.
Massive emotional appeal beyond this rational case to secure funds i.e. not 60701!

## Slide 31: Capability of this Ultimate UK simple.
At a maximum hand fired coal rate of 5500lb/hr , 60164 could sustain 2900-3000 IHP, more short term through boiler mortgage. This not a realistic estimate of daily capability, nor does 90mph running need it!
At a realistic firing at ca 3700lb/hr Blidworth type coal, ca 2100IHP, 60163+13 could get to York in 2’25” with a 90 mph limit, average 78mph (current semi fast schedule). Do you want to subject 60163 to this?
60164 could achieve this with ca. 600lb/hr less, or go 9 minutes faster on the same coal. No UK locomotive has ever run this hard, this fast for this long! Only the MILW 4-6-4s and 4-4-2s have. Robust design essential.
In this fantasy, it could go 5 minutes faster still with a 100mph limit (86mph average), burning 500lb/hr more coal.
Or climb Shap in 34 minutes from Carnforth, minimum 50 mph.
In my view, the operational case for such a more powerful new build is more about reserve and robustness than faster performance.

## Slide 32: Improving Smaller Class Outputs
Increasing efficiency via the measures described above are one option.
Power of current designs can be improved most easily by ca. 10% by a 10% increase in boiler pressure if:
  They are operating at less than the economic boiler limit in 25/60, say, <600lbs/sqft/hr and
  Adhesion ratio is well above, say, 4.4.
The KA, Patriot and Clan can be improved this way. And Flying Scotsman(!).
If this compromises adhesion ratio, mitigate by limiting maximum cut off (e.g. Lima, Santa Fe) (George V?) or reducing cylinder diameter.
Some move in this direction might be possible for other designs.
Increasing steam lap and reducing back pressure also help e.g. changing the very narrow Jubilee exhaust to a DC improved power by about 9%- why did the LMS not do this!? Fear of burning more coal? Could get 15% more power with ‘no one would know’ changes.

## Slide 33: What then should be the ASTT’s focus?
Emotion and nostalgia are the money spinners and trump rational behaviour on new designs. Go with the flow.
The ultimate Class 8/9 express design to give more reserve with 90 mph running? Tornado 2 20 years on?
Detail design improvements and more power for smaller main line classes, new builds and originals - looks worthwhile, and a number of options can be explored to deliver this.
A super BR4 for tourist lines? Any interest now? Not Bantam LGBT!
Ease of maintenance, reliability and safe operation. Are these the greatest prizes? How good are we? Should we research?
Cost saving efficiency not a goal for one of a kind classes. Delivery is.
Explore radical ideas in a lower risk narrow gauge not main line environment where development costs and risks too high?
Maintain the skill base - is this the real challenge?

## Slide 34: ASTT focus
Present
Future?
Passion
Knowledge
No money
Research
Advice
Advocacy
Engineering design
Novel ideas
Sharing
Business leadership
Marketing
Fund raising
Financing
Building
Regulatory
Operations management
Professional Staff
Dogsbodies

## Slide 35: A personal view: Anything is OK if it has 3 cylinders and looks like this (85% scale).